## Slide 1: ELEC-E8408 Hiking Tour Assistant Group B: Markus Mattsson Vilma Väisänen Teemu RauHA
AGENDA

## Slide 2: ELEC-E8408 Hiking Tour Assistant Group B: Markus Mattsson Vilma Väisänen Teemu RauHA
Overview (Context Diagram)
System Interfaces
Requirements
Test Report Summary
Design Report Summary
User Manual
Live Demo
AGENDA

## Slide 3
Overview

## Slide 4
Overview
INterfaces

## Slide 5
HW & SW
INterfaces
Component | Inputs | Outputs | Timing Constraints | Accuracy Metrics
LilyGo Smartwatch (ESP32) | Button press, Accelerometer (BMA423), touch screen | BLE data to Arduino, Display updates | Max response delay: 200ms | Step count: ±2% accuracy
Arduino Mega | BLE data from smartwatch, buttons | LCD updates, SRAM storage | Sync under 5 sec | N/A
LCD Screen (16x2, I2C) | I2C data from Arduino | Displays session data | Max update delay: 50ms | Readability at 30cm distance
Module | Inputs | Outputs | Data Format | Performance Constraints
Watch Firmware (ESP32) | Button press, Accelerometer | BLE sync data, UI display updates | JSON-like BLE payload | Max UI update delay: 200ms
Arduino Firmware | BLE session data | LCD output, SRAM storage | SRAM-stored stats | Sync within 5 sec
LCD Module | I2C data from Arduino | Displayed text | 16x2 character format | Response time < 50ms

## Slide 6
User Interface
Component | Inputs | Outputs | Interaction Method | Performance Constraints
LiLyGo Smartwatch UI | Button press, Touchscreen taps | 1,54-inch screen showing the GUI | Button & touchscreen | Max UI update delay: 200ms
Watch Accelerometer (BMA423) | User moving the watch | Step count data | Walking, jogging, running, etc | Step count accuracy ±2%
Arduino UI | Power on, button press | LCD screen displays session statistics | Turning power on & button press | Response time < 50ms

## Slide 7
Functional
Requirements
(watch)
FR-1-01: When turned off, after user presses the power button for 3 s (seconds), the watch shall turn on and start the initial program.
FR-1-02: Watch shall show the program standby view after turning on and keep the view on the screen until other required function is initiated.
FR-1-03: The standby view shall state the application name - “Hiking Assistant” and also present a touch-screen button for accessing the settings.
FR-1-04: While in the standby view, pressing the watch power button for 1 s shall start the hiking session.
FR-1-05: During an active hiking session, the watch shall count the steps taken by the user by listening to the interrupts from the BMA423 acceleration sensor.
FR-1-06: During an active hiking session the watch shall calculate distance traveled by multiplying the stride length with the steps count.
FR-1-07: Watch shall display steps count, distance, and time elapsed during an active hiking session. This session statistics shall be updated after each interrupt from the acceleration sensor.
FR-1-08: During an active hiking session, the watch shall allow the user to stop the hiking session by pressing the power button for 1 s.
FR-1-09: The watch shall save the hiking data to SRAM memory after the hike has been stopped.
FR-1-10: After stopping the hiking session, the watch shall attempt to synchronize with the Arduino via BLE. If the synchronization is unsuccessful, the watch will attempt 3 more times with 10 second intervals. If unsuccessful after re-attempts, the watch shall notify the user with a text or icon on the screen.
FR-1-11: Watch shall allow user configuration of stride length based on height in the settings.
FR-1-12: Watch shall display information in a readable format, ensuring optimal visibility in both dark and bright conditions.
FR-1-13: Watch shall allow the user to enable/disable automatic Bluetooth discovery for synchronization with Arduino.
FR-1-14: Watch shall have an option for manually initiating the BLE synchronization.
FR-1-15: When turned on, the watch shall turn off after user presses the power button for 3 seconds.

## Slide 8
Functional
Requirements
(Continued)
Watch-Arduino Sync Requirements (FR-2-XX)
FR-2-01: Watch shall initiate synchronization with Arduino at the end of a hiking session or upon user request.
FR-2-02: Watch shall transmit steps, distance, duration, and user information to Arduino via Bluetooth.
FR-2-03: Arduino shall acknowledge data receipt and confirm synchronization status to the watch.
FR-2-04: Watch shall notify the user whether synchronization was successful or failed.
FR-2-05: Watch may attempt automatic synchronization when in range of the Arduino, if enabled.
FR-2-06: Watch may establish a Wi-Fi connection with the Arduino if enabled from settings.
Arduino Requirements (FR-3-XX)
FR-3-01: Once turned on by attaching the power cable, the Arduino shall begin to poll the BLE sensor HM-10 for incoming transmissions.
FR-3-02: Arduino shall parse the received hiking session data into separate variables and store them into SRAM.
FR-3-03: Arduino shall calculate estimated calories burned using the stored hiking variables.
FR-3-04: Arduino shall adjust the calorie calculation formula if elevation data is available.
FR-3-05: Arduino shall display session statistics (steps, distance, duration, and calories) on the LED screen. All statistics may not be shown at the same time, and user shall have a way to scroll between different statistics.

## Slide 9
Performance
Requirements
Requirement | Value
Step count accuracy | ±2%, comparable to commercial smartwatches.
UI performance | Watch screen refresh rate at least 30 FPS. Maximum response time for user inputs (touch interactions) should be 200ms.
Battery | At least 12 hours continuous use.
Data Synchronization | BT synchronization between smartwatch and Arduino should be done in less than 5 seconds after initialization.
Environmental conditions | Temperature range to function in Finnish nature, -20°C to + 40°C.

## Slide 10
Test Report Summary
Objective:
Ensure HTA system meets all requirements through comprehensive testing.
Strategy:
Unit tests: Smartwatch and Arduino tests.
Integration tests: Synchronization and data transfer between watch and Arduino.
System tests: Validate complete system functionality and reliability.
Risk Mitigation:
Potential Bluetooth interference and data loss during sync.
Accurate distance calculation and calorie estimation.
Battery life and system reliability under various conditions.
Key Test Cases:
Watch Functionality: Start & stop sessions, step counting, distance calculation.
Data Synchronization: Bluetooth sync between watch and Arduino.
Arduino Processing: Data reception, calorie calculation, and display on LCD.
Goal:
Deliver a reliable and user-friendly HTA system that meets all requirements and performs effectively in real-world hiking environments.

## Slide 11
Design Report Summary
Strategy:
LiLyGo Smartwatch: Focus on data collection, user interaction, and BT communication.
Arduino Mega: Handle data processing, calorie calculation, and display of hiking statistics.
Key Design Elements
Bluetooth Communication: Reliable data transfer between smartwatch and Arduino, with error detection and retry mechanisms.
Data Processing: Efficient program for step counting, distance calculation, and calorie estimation.
User Interface: Intuitive design for easy navigation and real-time data display on both smartwatch and LCD screen.
Risk Mitigation:
Bluetooth Stability: Address potential interference and ensure robust data synchronization.
Resource Management: Optimize battery usage and memory allocation for prolonged operation.
Environmental Adaptability: Ensure functionality across varying outdoor conditions.
Goal:
Provide a comprehensive overview of the system's architecture, detailing how the software and hardware components are designed to meet the project's requirements.

## Slide 12
User Manual

## Slide 13
Live demo Time!
Hiking tour assistant

## Slide 14: THANK YOU!
Our repository can be found at:
github.com/Kalamadnas/E8408_Hiking_Assistant
End session
Steps: 3456

## Slide 15
Image sources:
https://www.biztechcs.com/blog/features-apple-watch-hiking-app-must-have/
https://chat.mistral.ai/